## Slide 1
Introduction to RTL Design
Register Transfer Level

## Slide 2
3
RTL Design
RTL Design Method
5.2

## Slide 3
3
RTL Design
RTL Design Method
5.2

## Slide 4: RTL Design
4
RTL Design Method: “Preview” Example
Soda dispenser
  c: bit input, 1 when coin deposited
  a: 8-bit input having value of deposited coin
  s: 8-bit input having cost of a soda
  d: bit output, processor sets to 1 when total value of deposited
a soda
s
a 25
25
50
coins equals or exceeds cost of 0 1 0 1 0
c d
0 1 0
tot:
25
Soda tot:
dispenser processor50
How can we precisely describe this processor’s behavior?
a
a
s
c d
Soda dispenser processor

## Slide 5: RTL Design
5
Preview Example: Step 1 – Capture High-Level State Machine
Declare local register tot
Init state: Set d=0, tot=0
Wait state: wait for coin
  If see coin, go to Add state
Add state: Update total value: tot = tot + a
  Remember, a is present coin’s value
  Go back to Wait state
In Wait state, if tot >= s, go to
Disp(ense) state
Disp state: Set d=1 (dispense soda)
  Return to Init state
Add
Disp
Init Wait
d=0 tot=0
d=1
Inputs: c (bit), a (8 bits), s (8 bits) Outputs: d (bit)
Local registers: tot (8 bits)
c
tot=tot+a c’*(tot<s)
s a
8 8
c d
Soda
dispenser processor
c’*(tot<s)’

## Slide 6: RTL Design
6
Preview Example: Step 2 – Create Datapath
Need tot register
Need 8-bit comparator to compare s and tot
Need 8-bit adder to perform tot = tot + a
Wire the components as needed for above
Create control input/ outputs, give them names
ld tot clr
8-bit
<
8-bit adder
8
8 8
8
s
a
Datapath
tot_ld tot_clr
tot_lt_s
Inputs : c (bit), a(8 bits) , s (8 bits) Outputs : d (bit)
Local reg isters: t ot (8 bits)
Wait
Add
Disp
Init
d=0
t ot=0
c‘ (tot<s)‘
d=1
c
tot= t ot+a c‘ *(tot<s)

## Slide 7: RTL Design
7
Controller’s inputs
  External input c (coin detected)
  Input from datapath comparator’s output,
which we named
tot_lt_s
Controller’s outputs
  External output d
(dispense soda)
  Outputs to datapath to load and clear the tot register
tot_clr
tot_ld
Controller tot_lt_s Datapath
c
d
s a
8 8
ld clr
tot
8-bit
<
8-bit adder
8
8 8
8
Preview Example: Step 3 – Connect Datapath to a Controller
s
a
Datapath
tot_ld tot_clr
tot_lt_s

## Slide 8: RTL Design
8
Preview Example: Step 4 – Derive the Controller’s FSM
Same states and arcs as high-level state machine
But set/read datapath control signals for all
datapath operations
and conditions
tot_lt_s
tot_clr
tot_ld
Controller
Datapath
c
d
s a
8 8
clr
ld tpt
8-bit
8-bit adder
8
8 8
8
s
a
<
Datapath
tot_ld tot_clr
tot_lt_s
Disp
Init Wait
d=0 tot_clr=1
c’* tot_lt_s’
d=1
Inputs::c, tot_lt_s (bit) Outputs:d, tot_ld, tot_clr (bit)
c
tot_ld=1 c’*tot_lt_s
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add

## Slide 9: RTL Design
9
Preview Example: Completing the Design
Implement the FSM as a state register and logic
  As in Ch3
  Table shown on right
Disp
Init Wait
d=0 tot_clr=1
c’* tot_lt_s’
d=1
Inputs::c, tot_lt_s (bit) Outputs:d, tot_ld, tot_clr (bit)
c
tot_ld=1 c’*tot_lt_s
c
d
tot_ld
tot_clr
tot_lt_s
Controller
Add

## Slide 10: RTL Design
10
High-Level State Machine
Soda dispenser example
  Not an FSM because:
    Multi-bit (data) inputs a and s
    Local register tot
    Data operations tot=0, tot<s, tot=tot+a.
  Useful high-level state machine:
    Data types beyond just bits
    Local registers
    Arithmetic equations/expressions
Init Wait
d=0 tot=0
Disp
d=1
Inputs: c (bit), a (8 bits), s (8 bits)
Outputs: d (bit)
Local registers: tot (8 bits)
c
tot= tot+a c’ (tot<s)
c’(tot<s)’

## Slide 11: RTL Design Step 1 Example: Laser-Based Distance Measurer
11
8
Example of how to create a high-level state machine to describe desired processor behavior
Laser-based distance measurement – pulse laser, measure time T to sense reflection
  Laser light travels at speed of light, 3*10 m/sec
  Distance is thus D = T sec * 3*108 m/sec / 2
Object of interest
D
2D = T sec * 3*108 m/sec
sensor
laser
T (in seconds)

## Slide 12: RTL Design
12
Step 1 Example: Laser-Based Distance Measurer
Inputs/outputs
  B: bit input, from button to begin measurement
  L: bit output, activates laser
  S: bit input, senses laser reflection
  D: 16-bit output, displays computed distance
sensor
T (in seconds)
laser
Laser-based distance measurer
16
D
to display
from button B
L
to laser
S
from sensor

## Slide 13: RTL Design Step 1 Example: Laser-Based Distance Measurer
13
Step 1: Create high-level state machine
Begin by declaring inputs and outputs
Create initial state, name it S0
  Initialize laser to off (L=0)
  Initialize displayed distance to 0 (D=0)
Laser- based distance measurer
D 16
to display
from button B
L to laser
S
from sensor
Inputs: B, S(1 bit each) Outputs: L (bit), D (16 bits)
S0
?
L = 0 (laser off)
D = 0 (distance = 0)
a

## Slide 14: RTL Design Step 1 Example: Laser-Based Distance Measurer
14
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits)
L = 0
D = 0
S1
?
B’ (button not pressed)
B
(button pressed)
S0
Add another state, call S1, that waits for a button press
  B’ – stay in S1, keep waiting
  B – go to a new state S2
Q: What should S2 do? A: Turn on the laser
a
a
Laser- based distance measurer
to display
S
D 16
from button B
L to laser
from sensor

## Slide 15: RTL Design Step 1 Example: Laser-Based Distance Measurer
15
S1
S0
L = 0
D = 0
S2
L = 1
(laser on)
S3
L = 0
(laser off)
B’
B
a
Add a state S2 that turns on the laser (L=1)
Then turn off laser (L=0) in a state S3
Q: What do next? A: Start timer, wait to sense reflection
a
Laser- based distance measurer
to display
S
D 16
from button B
L to laser
from sensor
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits)

## Slide 16: RTL Design
16
Step 1 Example: Laser-Based Distance Measurer
Stay in S3 until sense reflection (S)
To measure time, count cycles for which we are in S3
  To count, declare local register Dctr
  Increment Dctr each cycle in S3
  Initialize Dctr to 0 in S1. S2 would have been O.K. too
Lasre-based
distance measruer
to dispaly
S
D 16
from button B
L to laser
from sensor
S1
S3
S0
L = 0
D = 0
S2
L = 1
L = 0
Dctr = Dctr + 1 (count cycles)
Dctr = 0 (reset cycle count)
B
S (reflection)
?
a
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits) Local Registers: Dctr (16 bits)
B’ S’ (no reflection)

## Slide 17: RTL Design Step 1 Example: Laser-Based Distance Measurer
17
Once reflection detected (S), go to new state S4
 Calculate distance
8
 Assuming clock frequency is 3x10 , Dctr holds number of meters, so D=Dctr/2
After S4, go back to S1 to wait for button again
Lasre-based distance measruer
D 16
to dispaly
from button B
L to laser
S
from sensor
S3
S0 L = 0
D = 0
S2 L = 1
S1
Dctr = 0
B
S
L=0 D = Dctr / 2
Dctr = Dctr + 1 (calculate D)
S4
a
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits) Local Registers: Dctr (16 bits)
B’ S’

## Slide 18: RTL Design
18
Step 2: Create a Datapath
Datapath must
  Implement data storage
  Implement data computations
Look at high-level state machine, do three substeps
  (a) Make data inputs/outputs be datapath inputs/outputs
  (b) Instantiate declared registers into the datapath (also instantiate a register for each data output)
  (c) Examine every state and transition, and instantiate datapath components and connections to implement any data computations

## Slide 19: RTL Design Step 2 Example: Laser-Based Distance Measurer
19
Make data inputs/ outputs be datapath inputs/ outputs
Instantiate declared registers into the datapath (also instantiate a register for each
and transition, and
components and connections to implement any data computations
Datapath
data output)
(c) Examine every state Dreg_clr
instantiate datapath Dctr_clr
Dctr_cnt
Dreg_ld
S3
S0 L = 0
D = 0
S2 L = 1
S1
Dctr = 0
B
S
L=0 D = Dctr / 2 Dctr = Dctr + 1 (calculate D)
S4
Q
I
Dreg: 16-bit register
Q
Dctr: 16-bit up-counter
16
D
clear load
clear count
a
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits) Local Registers: Dctr (16 bits)
B‘ S‘

## Slide 20: RTL Design Step 2 Example: Laser-Based Distance Measurer
20
(c) (continued) Examine every state and transition, and instantiate datapath components and connections to implement any data computations
clear count
clear load
Q
Q
I
Dctr: 16-bit up-counter
Dreg: 16-bit register
16
D
Datapath
Dreg_clr Dreg_ld
Dctr_clr Dctr_cnt
16
16
>>1
a
S0 L = 0
D = 0
S2 L = 1
S1
Dctr = 0
B
S
L=0 D = Dctr / 2 Dctr = Dctr + 1 (calculate D)
S3 S4
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits) Local Registers: Dctr (16 bits)
B‘ S‘

## Slide 21: RTL Design Step 2 Example Showing Mux Use
21
Introduce mux when one component input can come from more than one source
T0 R = E + F
T1 R = R + G
Localregisters:
E, F, G, R (16 bits)
(a)
E
F G
A + B
R
add_A_s0 add_B_s0
(d)
2× 1 2×1
a
E
F G
A + B
R
(b)
E
F G
A + B
R
(c)

## Slide 22: RTL Design Step 3: Connecting the Datapath to a Controller
22
Laser-based distance measurer example
Easy – just connect all control signals between controller and datapath
300 MHz Clock
D
B
S
16
to display
from button
Controller
L
to laser
from sensor
Datapath
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_cnt
clear count
clear load
Q
Dctr: 16-bit up-counter
I Dreg: 16-bit
register
Q
16
D
Datapath
Dreg_clr Dreg_ld
Dctr_clr Dctr_cnt
16
16
>>1

## Slide 23: RTL Design
23
Step 4: Deriving the Controller’s FSM
FSM has same
structure as high- level state machine
Inputs/outputs all bits now
Replace data operations by bit operations using datapath
300 MHz Clock
D
L
S
16
to dispal y
B
from button
Controller
to laser
from sensor
Datapath
Dreg_clr
Dreg_ld
Dctr_clr
Dctr_cnt
Inputs: B, S
Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
S0
S1
S2
S3
B’
S’
B
S
S4
S3
S0
L = 0
D = 0
S2
L = 1
S1
Dctr = 0
Inputs: B, S (1 bit each) Outputs: L (bit), D (16 bits) Local Registers: Dctr (16 bits)
B’ S’
B
S
L=0 D = Dctr / 2 Dctr = Dctr + 1 (calculate D)
S4
a
Dreg_ld = 0
Dctr_clr = 0
Dctr_cnt = 0 (laser off) (clear D reg)
L = 0 L = 0
Dreg_clr = 1 Dreg_clr = 0
Dreg_ld = 0
Dctr_clr = 1
Dctr_cnt = 0 (clear count)
(laser on)
Dreg_ld = 0 Dreg_ld = 0
Dctr_clr = 0 Dctr_clr = 0
Dctr_cnt = 0 Dctr_cnt = 1
(laser off) (count up)
L = 1 L = 0 L = 0
Dreg_clr = 0 Dreg_clr = 0 Dreg_clr = 0
Dreg_ld = 1
Dctr_clr = 0
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)

## Slide 24: RTL Design Step 4: Deriving the Controller’s FSM
24
Using
shorthand of outputs not assigned implicitly assigned 0
a
S0
S1
S2
S3
B’
S’
B
S
S4
(laser off) (clear count) (laser on) (clear D reg)
L = 0 L = 0 L = 1 L = 0 L = 0
Dreg_clr = 1 Dreg_clr = 0 Dreg_clr = 0 Dreg_clr = 0 Dreg_clr = 0
Dreg_ld = 0 Dreg_ld = 0 Dreg_ld = 0 Dreg_ld = 0 Dreg_ld = 1
Dctr_clr = 0 Dctr_clr = 1 Dctr_clr = 0 Dctr_clr = 0 Dctr_clr = 0
Dctr_cnt = 0 Dctr_cnt = 0 Dctr_cnt = 0 Dctr_cnt = 1 Dctr_cnt = 0
(laser off) (load D reg with Dctr/2) (count up) (stop counting)
S0
S1
S2
S3
B
S
L = 1
(laser on)
S4
Inputs: B, S Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
B’ S’
L = 0 Dctr_clr = 1
Dreg_clr = 1 (clear count) (laser off)
(clear D reg)
L = 0
Dctr_cnt = 1
(laser off) (count up)
Dreg_ld = 1
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)

## Slide 25: RTL Design Step 4: Deriving the Controller’s FSM
25
D
16 300 MHz Clock
to display
from button B
Controller
Datapath
Dreg_clr
S0
S1
S2
S3
B
S
L = 1
(laser on)
S4
Inputs: B, S Outputs: L, Dreg_clr, Dreg_ld, Dctr_clr, Dctr_cnt
B’ S’
L = 0 Dctr_clr = 1
Dreg_clr = 1 (clear count) (laser off)
(clear D reg)
L = 0
Dctr_cnt = 1
(laser off) (count up)
Dreg_ld = 1
Dctr_cnt = 0
(load D reg with Dctr/2)
(stop counting)
Dreg_ld
Dctr_clr Dctr_cnt
clear count
clear load
Q
I
Dctr: 16-bit up-counter
Q
Dreg: 16-bit register
16
D
Datapath
L to laser Sfrom sensor
Dreg_clr
Dreg_ld
Dctr_clr Dctr_cnt
16
16
>>1

## Slide 26: RTL Design Design Challenge
25