## Slide 1
RTL Design Method Examples

## Slide 2
3
RTL Design
RTL Design Method
5.2

## Slide 3: RTL Design
4
RTL Example: Video Compression – Sum of Absolute Differences
Video is a series of frames (e.g., 30 per second)
Most frames similar to previous frame
 Compression idea: just send difference from previous frame
Digitized
frame 2
Digitized
frame 1
Digitized
frame 1
Frame 1
1 Mbyte 1 Mbyte 1 Mbyte
(b)
Only difference: UFO moving
Frame 1 Frame 2
a
Difference of
2 from 1
Frame 2
0.01 Mbyte
Just send
difference

## Slide 4: RTL Design
5
RTL Example: Video Compression – Sum of Absolute Differences
Need to quickly determine whether two frames are similar enough to just send difference for second frame
  Compare corresponding 16x16 “blocks”
    Treat 16x16 block as 256-byte array
  Compute the absolute value of the difference of each array item
  Sum those differences – if above a threshold, send complete frame for second frame; if below, can use difference method (using another technique, not described)
Frame 2
compare
Frame 1
Each is a pixel, assume represented as 1 byte (actually, a color picture might have 3 bytes per pixel, for intensity of red, green, and blue components of pixel)

## Slide 5: RTL Design RTL Example: Video Compression – Sum of Absolute Differences
6
go
!(i<256)
Want fast sum-of-absolute-differences (SAD) component
 When go=1, sums the differences of element pairs in arrays A and
B, outputs that sum
SAD
sad
256-byte array A
256-byte array B
integer

## Slide 6: RTL Design RTL Example: Video Compression – Sum of Absolute Differences
7
S0: wait for go
S1: initialize sum and index
S2: check if done (i>=256)
S3: add difference to sum, increment index
S4: done, write to output
sad_reg
B
A
go
SAD
sad
Inputs: A, B (256 byte memory); go (bit) Outputs: sad (32 bits)
Local registers: sum, sad_reg (32 bits); i (9 bits)
!go
S0
go
S1
sum = 0
i = 0
S3
S4 sad_reg = sum
S2
i<256
sum=sum+abs(A[i]-B[i]) i=i+1
(i<256)’
a

## Slide 7: RTL Design
8
RTL Example: Video Compression – Sum of Absolute Differences
Step 2: Create datapath
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sad_reg_ld
Datapath
sum
sad_reg
sad
AB_addr
A_data B_data
<256
9
32
8
8
8 8
32 32
32
i
–
+
abs
Inputs: A, B (256 byte memory); go (bit) Outputs: sad (32 bits)
Local registers: sum, sad_reg (32 bits); i (9 bits)
!go
S0
go
S1
sum = 0
i = 0
S3
S4 sad_reg=sum
S2
i<256
sum=sum+abs(A[i]-B[i])
i=i+1
(i<256)’
a

## Slide 8: RTL Design
9
RTL Example: Video Compression – Sum of Absolute Differences
Step 3: Connect to controller
Step 4: Replace high-level state machine by FSM
S0
S3
go’
go S1
go
AB_rd
Controller
i_lt_256
i_inc
i_clr
sum_ld
sum_clr
sad_reg_ld
sum
sad_reg
sad
AB_addr
A_data B_data
<256
9
32
8
8
8 8
32 32
32
i
–
+
abs
a
S4 sad_reg=sum sad_reg_ld=1
sum_ld=1; AB_rd=1
i=i+1 i_inc=1
S2
i<256 i_lt_256
sum=sum+abs(A[i]-B[i])
sum=0 sum_clr=1
i=0 i_clr=1
i_lt_256’

## Slide 9: RTL Design
Comparing software and custom circuit SAD
  Circuit: Two states (S2 & S3) for each i, 256 i’s 512 clock cycles
  Software: Loop (for i = 1 to 256), but for each i, must move memory to local registers, subtract, compute absolute value, add to sum, increment i – say about 6 cycles per
array item  256*6 = 1536 cyc les !(i<256)
  Circuit is about 3 times (300%) faster
  Later, we’ll see how to build SAD circuit that is even faster
10
RTL Example: Video Compression – Sum of Absolute Differences
S3
S2
i<256
sum=sum+abs(A[i]-B[i])
i=i+1
(i<256)’

## Slide 10: RTL Design Pitfalls and Good Practice
13
A B
R = 10 R = R + 1 Q = R
C
R = 20 D = Q + 1
D
D = D + 1
E
D = R
R ≤ 17
R > 17
Inputs:
Outputs: D (8-bits), Q (8-bits) Local Registers: R (8-bits)
F
Considering the high-level state machine shown to the right, what is the final value of D in state F?
1. 10
2. 11
3. 12
4. 17
5. 20

## Slide 11: RTL Design
12
Pitfalls and Good Practice
Common pitfall: Assuming register is update in the state it’s written
  All registers updates in each state will happen simultaneously
    On the next rising clock edge
Consider the FSM to the right:
  What is the final value of Q?
  What is the final state?
  Answer:
    Value of Q unknown
    Final state is C (not D)
  Why?
    State A: R=99 and Q=R happen simultaneously
    State B: R not updated with R+1 until next clock cycle, simultaneously with state register being updated

## Slide 12: RTL Design Pitfalls and Good Practice
13
A B
R = 10 R = R + 1 Q = R
C
R = 20 D = Q + 1
D
D = D + 1
E
D = R
R ≤ 17
R > 17
Inputs:
Outputs: D (8-bits), Q (8-bits) Local Registers: R (8-bits)
F
Considering the high-level state machine shown to the right, what is the final value of D in state F?
1. 10
2. 11
3. 12
4. 17
5. 20

## Slide 13: RTL Design
14
Pitfalls and Good Practice
Common pitfall: Reading outputs
  Outputs should only be written
  Solution: Introduce additional register, which can be written and read
T
S
P=P+B
P=A
(a)
Inputs: A, B (8 bits) Outputs: P (8 bits)
Inputs: A, B (8 bits) Outputs: P (8 bits) Local register: R (8 bits)
T
S
P=R+B
R=A P=A
(b)

## Slide 14: RTL Design
15
Pitfalls and Good Practice
Good practice: Register all data outputs
  In fig (a), output P would show spurious values as addition computes
    Furthermore, longest register-to-register path, which determines clock period, is not known until that output is connected to another component
  In fig (b), spurious outputs reduced, and longest register-to-register path is clear
+
R
B
P
(a)
+
R
Preg
B
P
(b)