## Slide 1: U204206B-Digital Electronics – Spring 2022
Introduction to Sequential Logic, Basic Storage Element
dd_vahid_slides_ch3
Digital-Electronics-Module-05
教材第5章

## Slide 2: Sequential Logic Design Introduction
3
Sequential circuit
 Simple example: a circuit that counts up in binary
3.1
Combinational digital circuit
1
a
1
F
Output depends not just on present inputs (as in b 0
combinational circuit), but on past sequence of inputs
  Stores bits, also known as having “state”
1
a
? F
b 0
Must know sequence of past inputs to know output
Sequential digital circuit

## Slide 3: Sequential Logic Design Example Needing Bit Storage
4
Flight attendant call button
  Press call: light turns on
    Stays on after button released
  Press cancel: light turns off
  Logic gate circuit to implement this?
Call Q
Cancel
Doesn’t work. Q=1 when Call=1, but doesn’t stay 1 when Call returns to 0
Need some form of “feedback” in the circuit
a
a
3.2
Bit Storage
Blue light
Call button
Cancel button
1. Call button pressed – light turns on
Bit Storage
Blue light
Call button
Cancel button
2. Call button released – light stays on
Bit Storage
Blue light
Call button
Cancel button
3. Cancel button pressed – light turns off
Notes: Attendant 乘务员

## Slide 4: Sequential Logic Design First attempt at Bit Storage
5
We need some sort of feedback
  Does circuit on the right do what we want?
    No: Once Q becomes 1 (when S=1), Q stays 1 forever – no value of S can bring Q back to 0
Q
S
t
S 1
0
t 1
0
Q 1
0
0
t
Q
S 1
0
t
S 1
0
1 Q
t
S 1
1
1
t
1 Q S 0
1 Q
a

## Slide 5: Sequential Logic Design Bit Storage Using an SR Latch
6
0
0
1
R=1
S=0
t
0
S 1
0
R 1
t 1
0
Q 1
0
Q
S (set)
SR latch
R (reset)
Does the circuit to the right, with cross-coupled NOR gates, do what we want?
 Yes! How did someone come up with that circuit? Maybe just trial and error, a bit of insight...
1
0 Q
1
1
t
0 Q
R=0
t
Q
S=0 S=1
R=0
0
1
0 1
t
Q
R=0
S=0
1
0
1
0
0
0
1
1
X
0
Recall…
a

## Slide 6: Sequential Logic Design Simple Example Using SR Latch for Bit Storage
7
SR latch can serve as bit storage in previous example of flight-attendant call button
  Call=1 : sets Q to 1
    Q stays 1 even after Call=0
  Cancel=1 : resets Q to 0
But, there’s a problem...
R
S
Q
Call but t on
Blue light
Cancel
but t on
Bit Storage
Blue light
Call button
Cancel button

## Slide 7: Sequential Logic Design SR Latch
8
What value with the output Q have at the indicated time?
1. 1
2. 0
3. Neither
4. Either
R=1
S=1
Q=0
t=0
R=0
S=0
Q=??
t=??
1
0
1
0
1
0
1
0
S
R
Q
t
??

## Slide 8: Sequential Logic Design
9
Problem with SR Latch
Problem
 If S=1 and R=1 simultaneously, we don’t know what value Q will take
Q may oscillate. Then, because one path will be slightly longer than the other, Q will eventually settle to 1 or 0 – but we don’t know which.

## Slide 9: Sequential Logic Design Solution: Level-Sensitive SR Latch
10
Add enable input “C” as shown
  Only let S and R change when C=0
    Enure circuit in front of SR never sets SR=11, except briefly due to path delays
  Change C to 1 only after sufficient time for S and R to be stable
  When C becomes 1, the stable S and R value
passes through the two AND gates to the SR
latch’s S1 R1 inputs.
R1
S
C
R
Level-sensitive SR latch S1
Q
Though SR=11 briefly...
...S1R1 never = 11
S
Q’
C
Q
R
Level-sensitive SR latch symbol
R1
S1
S
X
Y
Clk C
R
Level-sensitive SR latch
Q
0
1
0
0
R 1
C 0
1
S1 0
1
R1
1
S
a

## Slide 10: Sequential Logic Design Clock Signals for a Latch
11
How do we know when it’s safe to set C=1?
  Most common solution –make C pulse up/down
    C=0: Safe to change X, Y
    C=1: Must not change X, Y
    We’ll see how to ensure that later
  Clock signal -- Pulsing signal used to enable latches
    Because it ticks like a clock
  Sequential circuit whose storage components all use clock signals: synchronous circuit
    Most common type
    Asynchronous circuits – important topic, but left for advanced course
R1
X
Y
C
Clk
R
Q
Level-sensitive SR latch S
S1

## Slide 11: Sequential Logic Design Clock Signal Terminology
12
Clock period
  Time interval between pulses
    Above signal: period = 20 ns
Clock cycle
  Oone such time interval
    Above signal shows 3.5 clock cycles
Clock frequency
  1/period
    Above signal: frequency = 1 / 20 ns = 50 MHz
    1 Hz = 1/s
Freq | Period
100 GHz | 0.01 ns
10 GHz | 0.1 ns
1 GHz | 1 ns
100 MHz | 10 ns
10 MHz | 100 ns

## Slide 12: Sequential Logic Design Level-Sensitive D Latch
13
SR latch requires careful design to ensure SR=11 never occurs
D latch relieves designer of that burden
 Inserted inverter ensures R always opposite of S
R
S
D
C
D latch
Q
D Q’
C Q
D latch symbol

## Slide 13: Sequential Logic Design Problem with Level-Sensitive D Latch
14
D latch still has problem (as does SR latch)
  When C=1, through how many latches will a signal travel?
  Depends on for how long C=1
    Clk_A -- signal may travel through multiple latches
    Clk_B -- signal may travel through fewer latches
  Hard to pick C that is just the right length
    Can we design bit storage that only stores a value on the rising edge of
a clock signal?
rising edges
Clk

## Slide 14: Sequential Logic Design D Flip-Flop
15
Flip-flop: Bit storage that stores on clock edge, not level
One design -- master-servant
  Two latches, output of first goes to input of second, master latch has inverted clock signal
  So master loaded when C=0, then servant when C=1
  When C changes from 0 to 1, master disabled, servant loaded with value that was at D just before C changed -- i.e., value at D during rising edge of C
Clk
rising edges
Note: Hundreds of different flip- flop designs exist
D
D latch
Ds Qs’
Cs Qs servant
Q
Q’
D latch
Dm Qm
Cm
master
Clk
D flip-flop

## Slide 15: Sequential Logic Design D Flip-Flop
16
D
Q’
Q
D
Q’
Q
Symbol for rising-edge triggered D flip-flop
Symbol for falling-edge triggered D flip-flop
Clk
rising edges
Clk
falling edges
Internal design: Just invert servant clock rather than master
The triangle means clock input, edge triggered

## Slide 16: Sequential Logic Design D Latches and D Flip-Flops
17
D
D Q’
Q
Clk
What is the final value of the output Q given the following timing diagram? 1. 1
2. 0
3. Neither
4. 5

## Slide 17: Sequential Logic Design D Latches and D Flip-Flops
18
D
D Q’
Q
Clk
What is the final value of the output Q given the following timing diagram? 1. 1
2. 0
3. Neither
4. -2

## Slide 18: Sequential Logic Design D Flip-Flop
19
Solves problem of not knowing through how many latches a signal travels when C=1
  In figure below, signal travels through exactly one flip-flop, for Clk_A or Clk_B
  Why? Because on rising edge of Clk, all four flip-flops are loaded simultaneously -- then all four no longer pay attention to their input, until the next rising edge. Doesn’t matter how long Clk is 1.
Two latches inside each flip-flop
D1 Q1
D2 Q2
D3 Q3
D4 Q4
Y
Clk
Clk_A
Clk_B

## Slide 19: Sequential Logic Design D Latch vs. D Flip-Flop
20
Latch is level-sensitive: Stores D when C=1
Flip-flop is edge triggered: Stores D when C changes from 0 to 1
  Saying “level-sensitive latch,” or “edge-triggered flip-flop,” is redundant
  Two types of flip-flops -- rising or falling edge triggered.
Comparing behavior of latch and flip-flop:

## Slide 20: Sequential Logic Design Bit Storage Summary
21
D flip-flop |  |  |  |  | 
D | D latch Dm Qm Cm master |  |  | D latch Ds Qs’ Cs Qs servant | Q’
 |  |  |  |  | Q
Clk |  |  |  |  | 
S
R
D
Q
C
D latch
Feature: Only loads D value present at rising clock edge, so values can’t propagate to other flip-flops during same clock cycle. Tradeoff: uses more gates internally than D latch, and requires more external gates than SR – but gate count is less of an issue today.
Feature: SR can’t be 11 if D is stable before and while C=1, and will be 11 for only a brief glitch even if D changes while C=1. Problem: C=1 too long propagates new values through too many latches: too short may not enable a store.
S1
R1
S
Q
C
R
Level-sensitive SR latch
Feature: S and R only have effect when C=1. We can design outside circuit so SR=11 never happens when C=1.
Problem: avoiding SR=11 can be a burden.
R (reset)
S (set)
Q
SR latch
Feature: S=1 sets Q to 1, R=1 resets Q to 0. Problem: SR=11 yield undefined Q.

## Slide 21: Sequential Logic Design Basic Register
22
Typically, we store multi-bit items
  e.g., storing a 4-bit binary number
Register: multiple flip-flops sharing clock signal
  From this point, we’ll use registers for bit storage
    No need to think of latches or flip-flops
    But now you know what’s inside a register