## Slide 1: U204206B-Digital Electronics – Spring 2022
Combinational Logic Design Process and Common Combinational Components

## Slide 2: Digital Logic – Combinational Logic Combinational Logic Design Process
3
Step
Step 1 Capture the
function
Step 2 Convert to
equations
Step 3 Implement
as a gate- based circuit
Description
Create a truth table or equations, whichever is most natural for the given problem, to describe the desired behavior of the combinational logic.
This step is only necessary if you captured the function using a truth table instead of equations. Create an equation for each output by ORing all the minterms for that output. Simplify the equations if desired.
For each output, create a circuit corresponding to the output’s equation. (Sharing gates among multiple outputs is OK optionally.)
2.7

## Slide 3: Digital Logic – Combinational Logic
4
Combinational Logic Design Process Example: Three 1s Detector
Problem: Detect three consecutive 1s
10101011  0
in 8-bit input: abcdefgh
00011101  1
11110000  1
Step 1: Capture the function
  Truth table or equation?
 Truth table too big: 2^8=256 rows
case of three consecutive 1s
y = abc + bcd + cde + def + efg + fgh
Step 2: Convert to equation -- already done
Step 3: Implement as a gate-based circuit
 Equation: create terms for each possible a
a
a

## Slide 4: Digital Logic – Combinational Logic
5
Combinational Logic Design Process Example: Number of 1s Count
Problem: Output in binary on
two outputs yz the number of 1s on three inputs
010  01 101  10 000  00
Step 1: Capture the function
  Truth table or equation?
 Truth table is straightforward
Step 2: Convert to equation
  y = a’bc + ab’c + abc’ + abc
z = a’b’c + a’bc’ + ab’c’ + abc
 Step 3: Implement as a gate- based circuit
a
a
b c
a
b c
z
a
b c
a
b c
a b
b c
a b
y c

## Slide 5: Digital Logic – Combinational Logic More Gates
NAND: Opposite of AND (“NOT AND”)
NOR: Opposite of OR (“NOT OR”)
XOR: Exactly 1 input is 1, for 2-input
XOR. (For more inputs -- odd number of 1s)
XNOR: Opposite of XOR (“NOT XOR”)
2.8
x y F
0 0 1
0 1 0
1 0 0
x y F
0 0 0
0 1 1
1 0 1
x y F
0 0 1
0 1 0
1 0 0
x y F
0 0 1
0 1 1
1 0 1
1 1 0 1 1 0 1 1 0 1 1 1
y
x x
NAND NOR XOR XNOR
1
F y F x
y
F
x
y
1
x
x
y
F
y
NAND
NOR
0 0
NAND same as AND with power & ground switched
  Why? nMOS conducts 0s well, but not 1s (reasons beyond our scope) -- so NAND more efficient
Likewise, NOR same as OR with power/ground switched
AND in CMOS: NAND with NOT
OR in CMOS: NOR with NOT
So NAND/NOR more common
6

## Slide 6: Digital Logic – Combinational Logic More Gates: Example Uses
7

## Slide 7: Digital Logic – Combinational Logic Completeness of NAND
7
Any Boolean function can be implemented using just NAND gates. Why?
  Need AND, OR, and NOT
  NOT: 1-input NAND (or 2-input NAND with inputs tied together)
  AND: NAND followed by NOT
  OR: NAND preceded by NOTs
Likewise for NOR

## Slide 8: Digital Logic – Combinational Logic Number of Possible Boolean Functions
8
How many possible functions of 2 variables?
2
2 rows in truth table, 2 choices for each
2(22) = 24 = 16 possible functions
N variables
  2N rows
  2(2N) possible functions
a
0
b
0
0 or 1 2 choices
F
0 | 1 | 0 or 1 2 choices
1 | 0 | 0 or 1 2 choices
1 | 1 | 0 or 1 2 choices
 |  | 24 = 16 possible functions
a | b | f0 | f1 | f2 | f3 | f4 | f5 | f6 | f7 | f8 | f9 | f10 | f11 | f12 | f13 | f14 | f15
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0 a AND b a b a XOR b a OR b a NOR b a XNOR b b’ a’ a NAND b 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9: Digital Logic – Combinational Logic Decoders and Muxes
9
Decoder: Popular combinational logic building block, in addition to logic gates
  Converts input binary number to one high output
2-input decoder: four possible input binary numbers
  So has four outputs, one for each possible input binary number
Internal design
 AND gate for each output to detect input combination
Decoder with enable e
  Outputs all 0 if e=0
  Regular behavior if e=1
n-input decoder: 2n outputs
2.9
d0 1 d0 0 d0 0 d0 0
0 i0 d1 0 1 i0 d1 1 0 i0 d1 0 1 i0 d1 0
0 i1 d2 0 0 i1 d2 0 1 i1 d2 1 1 i1 d2 0
d3 0 d3 0 d3 0 d3 1
d0
d1
d3
i1 i0
d0
i0 d1
i1 d2
e d3
1
1
1
0
0
0
1
d0
i0 d1
i1 d2
e d3
1
1
0
0
0
0
0
i1’i0’
i1’i0
i1i0’ d2
i1i0

## Slide 10: Digital Logic – Combinational Logic Decoder Example
10

## Slide 11: Digital Logic – Combinational Logic N-bit Mux
10
i0 i1 i2
d0 d1 d2 d3 d4 d5 d6 d7
3x8 dec
What output of a 3x8 decoder will be asserted if i2i1i0 = 110?
1. d0 = 1
2. d3 = 1
3. d6 = 1
4. d7 = 1

## Slide 12: Digital Logic – Combinational Logic Multiplexor (Mux)
11
Mux: Another popular combinational building block
  Routes one of its N data inputs to its one output, based on binary value of select inputs
    4 input mux  needs 2 select inputs to indicate which input to route through
    8 input mux  3 select inputs
    N inputs  log2(N) selects
  Like a railyard switch

## Slide 13: Digital Logic – Combinational Logic Mux Internal Design
12
i0
i1
2×1
i0 i1
s0
1
d
2×1
i0 i1
s0
0
d
2×1
i0 i1
s0
d
0 s0
i0 (1*i0=i0)
d
i0
(0+i0=i0)
1
0
2x1 mux
i0 i1 i2 i3
s1 s0
d
d
i0
4 1
i1
i2
i3
s1 s0
4x1 mux
0
a

## Slide 14: Digital Logic – Combinational Logic Mux Example
12

## Slide 15: Digital Logic – Combinational Logic N-bit Mux
13
Example: Two 4-bit inputs, A (a3 a2 a1 a0), and B (b3 b2 b1 b0)
 4-bit 2x1 mux (just four 2x1 muxes sharing a select line) can select between A or B
s0
i1
i0 2 1
d
s0
i1
i0 2 1
d
s0
i1
i0 2 1
d
i0
i1 s0
2 1
d
a3 b3
a2 b2
a1 b1
a0 b0
s0
s0
4-bit
I0 2x1
D
I1
s0
C
4
4
A
4
B
c3
c2
c1 c0
is short for
Simplifying notation: 4
C

## Slide 16: Digital Logic – Combinational Logic N-bit Mux
14
s0
4-bit
I0 2x1
D
I1
s0
C
4
4
A
4
B
If A=5, B=2, what is the output of the 4-bit 2x1 mux if s0 = 1?
1. 0
2. 5
3. 2
4. 7

## Slide 17: Digital Logic – Combinational Logic N-bit Mux Example
Four possible display items
  Temperature (T), Average miles-per-gallon (A), Instantaneous mpg (I), and Miles remaining (M) -- each is 8-bits wide
  Choose which to display using two inputs x and y
  Use 8-bit 4x1 mux
15

## Slide 18: Digital Logic – Combinational Logic Non-Ideal Gate Behavior -- Delay
16
Real gates have some delay
 Outputs don’t change immediately after inputs change

## Slide 19: Digital Logic – Combinational Logic Encoders
17
Encoder: Combinational logic building block with opposite functionality of decoder
  Outputs binary encoding for input signal that is 1
  4x2 encoder would have four inputs and 2 outputs
What if two inputs are 1?
  Can use a priority encoder
  Gives priority to the highest input that is 1, and outputs binary encoding for that input
  Example: If d3=1 and d1=1, will output e0=1 and e1=1 because d3 has priority
1 d0 0 d0 0 d0 0 d0
0 d1 e0 0 1 d1 e0 1 0 d1 e0 0 0 d1 e0 1
0 d2 e1 0 0 d2 e1 0 1 d2 e1 1 0 d2 e1 1
0 d3 0 d3 0 d3 1 d3
1 d3
1 d1 e0 1
0 d2 e1 1
0 d0

## Slide 20: Digital Logic – Combinational Logic In Class Exercise
18
Design a 4x2 encoder using AND, OR, and NOT gates.